## Slide 1
15.B Mounting & Unmounting FS
access the contents of file systems by adding
and removing file systems from the file system hierarchy.

## Slide 2
Mount
Using the name of the device file in /dev
UUID written to the file system, universally-unique identifier.

## Slide 3
Identifying the Block Device
[root@host ~]# lsblk
NAME MAJ:MIN RM SIZE RO TYPE MOUNTPOINT
vda 253:0 0 12G 0 disk
├─vda1 253:1 0 1G 0 part /boot
├─vda2 253:2 0 1G 0 part [SWAP]
└─vda3 253:3 0 11G 0 part /
vdb 253:16 0 64G 0 disk
└─vdb1 253:17 0 64G 0 part

## Slide 4
Mounting by Block Device Name
[root@host ~]# mount /dev/vdb1 /mnt/data

## Slide 5
Mounting by File-system UUID
[root@host ~]# lsblk -fp
NAME FSTYPE LABEL UUID MOUNTPOINT
/dev/vda
├─/dev/vda1 xfs 23ea8803-a396-494a-8e95-1538a53b821c /boot
├─/dev/vda2 swap cdf61ded-534c-4bd6-b458-cab18b1a72ea [SWAP]
└─/dev/vda3 xfs 44330f15-2f9d-4745-ae2e-20844f22762d /
/dev/vdb
└─/dev/vdb1 xfs 46f543fd-78c9-4526-a857-244811be2d88

## Slide 6
Mounting by File-system UUID
[root@host ~]# mount UUID="46f543fd-78c9-4526-a857-244811be2d88" /mnt/data

## Slide 7
AUTOMATIC MOUNTING OF REMOVABLE STORAGE
DEVICES
/run/media/USERNAME/LABEL

## Slide 8
unmounting
[root@host ~]# umount /mnt/data

## Slide 9
unmounting
[root@host ~]# cd /mnt/data
[root@host data]# umount /mnt/data
umount: /mnt/data: target is busy.

## Slide 10
unmounting
[root@host ~]# lsof /mnt/data